## Slide 1: Computer Architecture Fundamentals of Quantitative design and analysis
Name: Eddy Kimani
Registration Number: SCT212-0596/2021

## Slide 2: Introduction
Since the late 1970s till the early 200s, computers have had a rapid advance in cost and performance, achieving an annual growth rate of 52%
This corresponds with Moore’s law, which predicted the doubling of transistors in chips after every 2 years
A new design approach known as RISC(Reduced Instruction Set Computer) architecture was also created, which used simpler instruction sets compared to its predecessors

## Slide 3: Classes of Computers
Personal Mobile Devices -> These devices try to maximize battery life and performance over a small form factor. Examples include smart phones and tablets
Desktop Computing -> These devices are built for tasks that require much more processing power that what a typical personal mobile device can handle. They focus on balancing between price and performance in tasks like web browsing, writing documents and playing graphics intensive games
Servers -> These devices focus on handling high throughput, since they are meant to handle a large volume of data and requests 24/7
Clusters/Warehouse computers -> These are groups of interconnected servers that work together as a single system. These are the massive data centers running cloud services. They are designed for massive scalability, power efficiency, fault tolerance and storage capacity
Embedded computers -> These are the systems integrated in everyday machines from cars to appliances to industrial equipment. They are specific purpose computers needed to be highly reliable and energy efficient

## Slide 4: Parallelism
Due to limitations in power consumption, the industry started shifting to parallelism, where instead of focusing on the single processor performance of a single chip, multiple processors (cores) were introduced on one chip
The classes of parallelism include:
  Data level parallelism, where multiple data points are operating at once
  Task level parallelism, where independent tasks are executed simultaneously
  Request level parallelism, where many independent requests are handled
Categories of parallel architecture include:
  Single Instruction Single Data (SISD) -> A single processor executes a single instruction at a time on a single data point
  Single Instruction Multiple Data (SIMD) -> A single instruction is applied to multiple data points simultaneously
  Multiple Instruction Single Data (MISD) -> Multiple instructions are carried out a single data point
  Multiple Instruction Multiple Data (MIMD) -> Multiple instructions are connected to multiple data points concurrently

## Slide 5: Defining Computer Architecture
Different computer architectures have evolved to meet specific user needs and requirements
The instruction set architecture is the actual programmer visible instruction set in the book that serves as the boundary between software and hardware
The most common types of instruction set architectures include:
  X86 -> This is the most influential architecture which has been implemented in most modern devices we use today. The architecture has evolved over the years from 16 bits to 64 bits
  ARM -> This is a newer architecture designed with a focus on simplicity and power efficiency in mind

## Slide 6: Trends in Technology
If an instruction set architecture is to be successful, it must be designed to survive rapid changes in computer technology
There have been 5 implementation technologies, which have changed at a dramatic pace:
  Integrated circuit logic technology -> Transistor density has doubled every 18-24 months, according to Moore’s law
  Semiconductor DRAM -> Memory capacity has grown 25 – 40% per year
  Semiconductor Flash -> This is the fast non-volatile memory used in SSDs and mobile devices that grows at 50 – 60% per year
  Magnetic Disk Technology -> Traditional hard drives have improved in storage capacity but lag in speed
  Network Technology -> Network performance depend on the performance of switches and the transmission system
Data transfer speed (bandwidth) improves much faster than response time (latency)

## Slide 7: Trends in Power and Energy in Integrated Circuits
Power consumption is still the main constraint in CPU design
However, there are techniques that are being used to improve energy efficiency. They include:
  Dynamic voltage and Frequence Scaling (DVFS) -> This adjusts power based on a given workload
  Turning off idle components which saves energy when not in user
  Efficient cooling techniques to prevent overheating in high-performance systems
  Using multicore processors instead of increasing the clock speeds of a single processor

## Slide 8: Trends in Cost
Over the years computing power has become cheaper than ever, but development costs are rising
Moore’s law is slowing down, making cost efficiency more important
This has been caused by:
  The complexity of manufacturing smaller transistors -> More transistors equals higher cost
  Memory and storage prices -> DRAM and Flash semiconductors are becoming cheaper
  Energy consumption -> Power efficiency reduces operational costs
  Demand for specialized hardware